# Calc W. Of E. Probability Map (Calc Weights of Evidence Probability Map)
## Description
This container calculates a probability map applying the Weights of Evidence method.
## Inputs
Name	Type	Description
Landscape	Categorical Map Type	Map of land use and cover classes.
Weights	Weights Type	Weights of Evidence coefficients.
Transitions	Transition Set Type	List of transitions for which spatial probability maps will be calculated.

## Optional Inputs
Name	Type	Description	Default Value
Cell Type	Cell Type Type	Data cell type.	Unsigned 8 Bit Integer
Null Value	Null Value Type	Null value.	Default

## Output
Name	Type	Description
Probabilities	Map Type	Map of probabilities.

## Group
Map Algebra
## Notes
The spatial transition probability maps depict the probability of a cell at position (x,y) to change from state i to state j. The spatial transition probabilities are calculated for each cell on the landscape raster map and for each specified transition. Dinamica employs the Weights of Evidence method, which uses a general polytomous logistic equation (see equation) to select the most favorable areas for each type of transition. The calculations are made using spatial variables stored in the GIS.
## Internal Name
CalcWOfEProbabilityMap
## Usage examples
See practical examples of this functor in Lesson 18: Building a land-use and land-cover change simulation model