# Mux Value
## Description
This functor initiates and feeds back a loop variable containing a value. In the beginning of the first iteration, it reads the input value from the initial port.
## Inputs
Name	Type	Description
Initial	Real Value	The initial value.
Feedback	Real Value	Value generated from model step.

## Optional Inputs
## Outputs
Name	Type	Description
Value	Real Value	The output value.

## Group
Control
## Notes
The use of this functor is critical for the development of dynamic models whose variables are dynamically updated as a result of the model feedback.
Muxes must always be placed directly inside loop containers like Repeat, For, For Each Category etc.

## Internal Name
MuxValue