# Extract Categorical Map Attributes
## Description
This functor calculates basic statistics from a map for each area delimited by a class. The result is returned in a table contains the extracted classes and their corresponding attributes.
## Inputs
Name	Type	Description
Map	Map	Map whose attributes will be extracted.
Categorical Map	Categorical Map	Map whose classes will be used to delimit the calculation areas in the input.

## Optional Inputs
Name	Type	Description	Default Value
Extract Statistical Attributes	Bool	If true, statistical attributes will be calculated.	True

## Outputs
Name	Type	Description
Attributes	Table	Table containing the attributes extracted from a map.

## Group
Map Algebra
## Notes
This functor analyzes all map layers. The resulting table refers to all of them.
The functor returns a table mapping classes and attributes to their corresponding attribute value. This table has the following format.
Column Name	Key or Data?	Column Type	Description
“Category”	Key	Real	The map category
“Attribute”	Key	Real	The attribute key
“Value”	Data	Real	The attribute from the map

Each “Attribute” has a predefined name. This name can be used to retrieve the corresponding attribute in Calculate Map, Calculate Categorical Map, Calculate Value and Calculate Lookup Table.
If it is not possible to determine any of these attributes, the corresponding entry in the output table is left blank. It determines the maximum and the minimum values only when there is at least one non null cell on the map for the given class.
### Dynamic attributes
Key	Predefined Name	Description
8	“nullCells”	number of null cells
9	“nonNullCells”	number of non null cells
10	“minCell”	minimum value (excluding null cells)
11	“maxCell”	maximum value (excluding null cells)
12	“cellSum”	sum of the values (excluding null cells)

### Statistical attributes
Key	Predefined Name	Description
13	“meanCell”	average (excluding null cells)
14	“cellVar”	variance (excluding null cells)
15	“cellStd”	standard deviation (excluding null cells)
16	“modeCell”	mode (excluding null cells)
17	“medianCell”	median (excluding null cells)
18	“uniqueCells”	total unique occurrences (excluding null cells)

## Internal Name
ExtractCategoricalMapAttributes