# Load Categorical Map
## Description
This functor loads a map from a file whose cell identifiers represent categories. The file name and its path must be specified. If the map found at this path does not have category identifiers, this functor will automatically determine its category identifiers.
## Inputs
Name	Type	Description
Filename	Map Filename	Name of the file that contains the map to be loaded. Dinamica automatically determines the file format from a selected file extension.

## Optional Inputs
Name	Type	Description	Default Value
Load As Sparse	Bool	If true, the map is loaded as a sparse image. Sparse images have the advantage of storing only the cells containing non-null values, but they have diminshed access time.	False
Define Null Value	Bool	This flag forces the cells with the same value of the “Null Value” parameter to be treated as a null cell. This is particularly useful for assigning a missing null value to a GeoTiff data.	False
Null Value	Int	Value used to represent null cell. The “Define Null Value” flag must be set in order to define a null value. This is particularly useful for assigning a missing null value to a GeoTiff data.	0
Suffix Digits	Non Negative Int	Number of digits used to represent the image file name suffix.	0
step	Non Negative Int	Current step or model iteration. Files with the same name and numbered suffixes will be loaded sequentially according to the model step.	None
Workdir	Workdir	Workdir folder path.	None

## Outputs
Name	Type	Description
Map	Categorical Map	The map loaded by the functor.

## Group
Input/Output
## Notes
See also Load Map for loading maps whose cells represent categories.
For a list of file formats that Load Categorical Map can load, the supported projections and datums, check the supported map formats.
## Internal Name
LoadCategoricalMap